## Slide 1: Automating Aerial Imaging
Christopher Lippitt
Grant Fraley

## Slide 2: The Beginning
SDSU CESAR
TerraPan Labs
  Spinoff of CESAR
  Camera + Velcro + RC Airplane
  Portable, flexible, remote sensing
  “Plan-Fly-Map”
SDSU CESAR
UAV
Image Management

## Slide 3: F-Planar: Plan
SDSU CESAR
UAV
Image Management
Interactive flight planning
Automated waypoint generation
Supports any frame camera
Output to UAV autopilot
Output to KML, GPX, and others for manned flight

## Slide 4: LOUIS: Fly
SDSU CESAR
UAV
Image Management
Autonomous unmanned imaging system
30 min duration with ~ 2sq. mile coverage at ~7cm
RGB, UV, NIR 10 megapixel sensor (3648x2736)
Optically stabilized Leica Lens
GPS + inertial data
Laptop ground control station
2.4 GHZ Remote Control (RC)
Week long training on RC piloting and system operation

## Slide 5: Bloodhound: Map
Directifi
  Rapid orthocorrection desktop software
Bloodhound
  High precision mosaic and terrain generation in the “cloud”
    1-2 pixel horizontal accuracy
    ~2 pixel vertical accuracy
  Fully automatic
SDSU CESAR
UAV
Image Management

## Slide 6: Bloodhound: Map
SDSU CESAR
UAV
Image Management
Example map: Mean projection error 0.865278 pixels, 0.6 mile coverage, 5cm resolution

## Slide 7: Bloodhound: Map
SDSU CESAR
UAV
Image Management
Example map: Mean projection error 0.865278 pixels, 0.6 mile coverage, 5cm resolution

## Slide 8: FAA & UAVs in National Airspace
FAA Certificate of Authorization (COA)
Issued for 1 year, can ‘renew’ certificate once
Currently available to Government agencies only
  State, local, and Federal agencies
  State Universities
  Law enforcement, first responders
Application assistance available
SDSU CESAR
UAV
Image Management

## Slide 9: TerraPan Labs: Moving Forward
Managing multi-temporal archives of imagery
Post-earthquake change analysis project
  Monterrey Naval Post-graduate School
  SDSU
  TerraPan Labs
    Interactive data viewer
    On-the-fly change analysis
    Visual management of enormous image databases
SDSU CESAR
UAV
Image Management

## Slide 10: ImageTank
Extending the web-based model of tiles and zoom levels
  Layers of data with movable ordering
    Handles temporal or overlapping imagery
  Breaking free of the single mosaic
  On-the-fly analysis and visualization of results
SDSU CESAR
UAV
Image Management

## Slide 11: ImageTank
Subscription-based cloud service for hosting and processing of imagery
Social (public) or private sharing of views into your database
Low resource footprint for municipalities and organizations
SDSU CESAR
UAV
Image Management

## Slide 12: ImageTank: Comments?
Imagery management solutions
Sharing of imagery publicly or privately
Collaborative analysis
IT Resources (storage, security)
SDSU CESAR
UAV
Image Management

## Slide 13: Questions?
More info:
Lippitt@TerraPanLabs.com
Fraley@TerraPanLabs.com
www.TerraPanLabs.com
Facebook.com/TerraPanLabs
Twitter.com/TerraPanLabs