# GUIDELINES FOR THE SUBMISSION OF DIGITAL MAPS

# Introduction

The <<jurisdiction>> maintains a Geographic Information System (GIS) for use by many departments for a variety of public-service uses.  An important public service that will be tied to the maintenance of the GIS is the dispatching of emergency first responders (such as police, fire, and paramedics).

We rely on public safety agencies for keeping our communities safe.  Planning and preparedness are required to help reduce the loss of life and/or property from natural and human-caused emergencies.  Because all emergencies have a geographic component (a location), a well-maintained GIS can help public safety agencies by providing first responders with the best information to make optimized safety decisions under stressful conditions.

In addition, GIS also assists with other important public-service uses, such as current and long range planning, and public works facility and asset inventory and maintenance.

To maintain the efficiency and effectiveness of these public safety/public service activities, the <<jurisdiction>> requires tentative maps, final maps, and improvement plans to be submitted in digital format so that additions and updates to land records and infrastructure in the GIS database are accomplished as quickly and efficiently as possible.  This requirement is in addition to hardcopy submission requirements.  The intent of these standards is to enable the required hardcopy and digital submission to be produced from the same digital data without significant modification.  (Those modifications include a global specification of a ‘CONTINUOUS’ line type, and in some cases the aggregating/disaggregating of layer contents to conform to the standards’ layer listing (See Table A).)

Additionally, the submitted digital data may be used for computational purposes in reviewing the map, maintaining digital land bases, or used in a document management system.  A disclaimer of liability will be placed on all digital files and file copies.  The recorded hardcopy will continue to be the official document.

# Format Requirements

The format for digital submission of specified plans and maps shall be one of the following:

AutoCad DWG  (Release 2000 or newer)

# DXF

# ESRI shapefile

ESRI personal geodatabase

XML

# Submission Requirements

- The model space of the submitted drawings should contain the entire project (showing project boundary, lot lines, rights-of-way, improvements, etc.), and it should not be divided into sheets (used for plotting purposes.)

- No externally referenced data is permitted. All data referenced is to be included in the file submitted.

- No lines are to be constructed with deliberate gaps.

- Maps will be oriented to geographic north.

- Annotation layers will be used to provide attribute data on each object where text is requested.  Text insertion points are to be middle justified.  Where text relates to an area, the text insertion point must lie within enclosed area boundary.

- Blocks will not be permitted as a valid data element for point feature symbology.

- Units will be decimal units.

- Scale will be 1:1

# Data Layer Requirements

Based on the requirements of the specific project, the submitted digital file will contain a certain number of layers from Table A. The entities in the named layers in Table A are assumed Proposed (to be done by this drawing). Layers containing other than proposed entities shall add to the layer name “-existing” (to remain), “-remove” (existing to be removed), “-abandon in place” (applied mostly to subsurface structures), “-Old” (centerlines of record etc.), and/or “-Future” (alignments/facilities not done by this set of drawings). In addition to the digital file, the applicant will also submit an edited version of the attached spreadsheet (see Appendix A – Example of LayerNamesCrossTab.xls) which lists the Applicants’ internal layer names with the corresponding layer name in the agency’s standard. This will result in a ‘translation table’ being created, so that the agency can extract and name file layers for inclusion into the agency’s GIS database.

# TABLE A.

Note:  All other data not required by the GIS, but useful to the enterprise, can be transmitted on other logical data layers.

# Digital File Submission Procedure

The digital file will be submitted by CD, DVD, or via ftp upload to the following addresses:

<< Agency Mailing Address>>

<<Agency ftp site, including username and password>>

# File Naming Conventions

Filenames for digital submission shall be appropriately assigned based on the alphanumeric project numbers assigned at the time the application is received by the <jurisdiction> (Insert Example: Project.dxf or Project.gdb).  For projects with multiple exhibits, i.e., General Plan Amendment and Rezone, each file shall be named with the appropriate abbreviations (Example: GP_Project.dxf or RZ_Project.gdb).  The following is a listing of standard County abbreviations. Other naming conventions may be required by the local jurisdiction. Contact the local jurisdiction for specific naming conventions:

# TM = Tentative Map

TPM = Tentative Parcel Map

SM = Final Subdivision Map

PM = Final Parcel Map

IP = Improvement Plan

GPA = General Plan Amendment

RZ = Rezone

# Media Requirements

The following methods of data transfer are considered acceptable for digital submission of data:

- CD or DVD media

- Via email (subject to local agency approval)

- File Transfer Protocol (FTP) (if available)

# Explanatory Data

All digital data will require an accompanying metadata text file.  The file will be in ASCII file (.txt extension) format using the same naming convention as the digital data file being submitted.  This file will contain the following information:

# Project Name:

# File Name:

# Date:

# Contact Name:

# Contact Phone:

# Contact Email:

Master Parcel Number and adjacent current parcel numbers (APN):

Layer name translation table:

Epoch:

Control point order accuracy:

Vertical datum referenced:

# Data Integrity Requirements

The following requirements pertain to the mathematical integrity of the geometric data.  This section is considered optional for tentative maps (items 1-7 are applicable to final maps; 4-7 are applicable to engineering plans).

1.  The maximum error allowable between theoretically coincident points will be 	.03 feet (9mm).

2.  The maximum error allowable between points on a line and the line will be .02 	feet (6mm).

3.  The difference between distances calculated by the inverse between the 	coordinates of points in the digital submission and the annotated distance shall not 	exceed .01 feet (3mm).

4.  The difference in seconds between the rounded value of the inverse 	coordinates of points in the digital submission and the annotated bearings shall 	not exceed +/- one second.

5.  Logical areas will be transmitted as a closed figure.  Line end nodes will be 	snapped to adjoining line node to ensure this requirement.

6.  Annotation submitted digitally will be identical to annotation submitted on the 	hardcopy maps.  Draw lines will represent their annotated values.

7.  When displaying coordinates, the entire number to the fifth decimal place for the coordinate will be shown (i.e., no constants will be applied).

# Horizontal Control

1.  The County of San Diego maintains horizontal control systems of varying accuracy. For the purposes of this standard, the County’s California Spatial Reference Network (Real Time Network) or first order or better control points will be used.

2.  Subdivision Mapping

a) The project boundary shall be tied to the County of San Diego’s horizontal control system. The Licensed Surveyor or Civil Engineer authorized to practice surveying shall be required to tie the Project Boundary to a minimum of two such control monuments in accordance with the County of San Diego’s Subdivision Regulations.

b)  All mapping control shall conform to the provisions of the California Resources Code, Section 8801 et seq. If coordinates are shown, 1) they shall be based on the California State Plane Coordinate System, Zone 6, NAD83, in US survey feet, and 2) the map shall call out the order and show the epoch of the control points used in the survey. If a Geodetic Grid factor is shown, the appropriate elevation shall also be stated for the conversion point.

- Engineer Plans and GIS Maps

The Licensed Surveyor or Civil Engineer shall be required to tie the Project to a minimum of two County of San Diego first order or better control monuments. Coordinates of the control points shall be shown and, 1) they shall be based on the California State Plane Coordinate System, Zone 6, NAD83, in US survey feet, and 2) shall call the epoch of the control points used in the survey.

# Review of Digital Data

All digital data will be reviewed for the following criteria:

1.  Correct layering.

2.  No duplicate linear or point elements.

3.  Closure of the geometry of all logical areas.

4.  Verification that digital and hardcopy maps are consistent.

5.  Correct geographical position (i.e., correct coordinate values for final 	submissions).

The submitting party will be responsible for correcting any errors and delivering the new correct digital file prior to approval by the <<jurisdiction>>.

APPENDIX A – Example of LayerNamesCrossTab.xls

This table provides a translation of layer naming by the submitting entity to the standard layer naming convention.

| STANDARD LAYER NAME | SUBMITTED LAYER NAME |
| --- | --- |
| …. |  |
| ….. |  |
| LOTLINE | 198Lot |
| LOTNUM | 198Lnum |
| MEDIAN | 198med |
| METEBNDS | survtext |
| MONTEXT | montext |
| MONUMENT | surv-x |
| NEWBLDGFP | bld-out |
| NEWESMENT | n-ease |
| …. |  |
| …. |  |

APPENDIX B – Data Layer and Map Submittal Type

The following table lists the layer contents of the required files for each type of map submission.

| LAYER | DATA OR FEATURE | Fire Pre-plan | Tent. Maps | GP/ZC Map | Imprv Plan | Final / Pcl Maps |
| --- | --- | --- | --- | --- | --- | --- |
| BLDACCESS | Building Access Locations | X |  |  | X |  |
| BLOFF | Blow-offs |  | X |  | X |  |
| BLOFFTXT | Blow-offs Text |  | X |  | X |  |
| BNDTXT | Boundary text, survey calls, etc. |  | X |  |  | X |
| CL | Street Centerlines |  | X |  | X | X |
| CPLINE | Community Plan Boundary Line |  |  | X |  |  |
| CPTEXT | Community Plan Designation |  |  | X |  |  |
| CURBGUTTER | Curbs and Gutters |  | X |  | X |  |
| DECOMGRANITE | Outline of Decomposed Granite |  | X |  | X |  |
| DETBASIN | Proposed Detention Basin |  | X |  | X | X |
| DRIVEWY | Driveway Locations | X | X |  | X |  |
| ELEV | Elevator Locations | X |  |  | X |  |
| ENGRDS | Engineered Roads (curb-to-curb) | X | X |  | X |  |
| EXESMNT | Existing easements |  | X |  | X | X |
| FACILITY | Laundry, Security, Hazardous Materials Storage, Other Buildings | X |  |  |  |  |
| FENCE | Fences | X |  |  | X |  |
| FIRECON | Fire Dept. Connection to Water Tank | X |  |  | X |  |
| GATE | Gates (locked & unlocked) | X |  |  |  |  |
| GOLF | Golf Course Features (greens, fairways, tees, clubhouse) | X |  |  | X |  |
| GPLINE | General Plan Boundary Line |  |  | X |  |  |
| GPS-POINT | County Control Points |  | X |  | X | X |
| GPS-TXT | Control Point description |  | X |  | X | X |
| GPTXT | General Plan Designation |  |  | X | X |  |
| HARDSURFACE | Outline of Hard Surface Areas not Composed of Decomposed Granite |  | X |  | X |  |
| HYDRANT | Fire Hydrants, Standpipes | X |  |  | X |  |
| KNOX | Knox Box Locations | X |  |  | X |  |
| LOTLINE | Lot Lines | X | X | X | X | X |
| LOTNUM | Lot Numbers |  | X | X | X | X |
| MEDIAN | Outline of Medians | X | X |  | X |  |
| METEBNDS | Traverse information |  | X |  | X | X |
| MONTEXT | Monument Description |  | X |  | X | X |
| MONUMENT | Monument Point |  | X |  | X | X |
| NEWBLDGFP | New Building Footprints | X | X |  | X | X |
| NEWESMENT | New Road & Open Space Easements (private & public) |  | X |  | X | X |
| NEWESTXT | New Easement descriptions |  | X |  | X | X |
| PARKING | Parking (Curb-to-Curb) | X | X |  | X | X |
| PEDRAMP | Pedestrian Ramp | X | X |  | X |  |
| PROPCONT | Proposed Contours |  | X |  |  |  |
| ROW | Street right-of-way | X | X |  | X | X |
| SALAT | Sewer Lateral |  | X |  | X |  |
| SALIFT | Sanitary Sewer Lift Station |  | X |  | X |  |
| SALIFTTXT | Sanitary Sewer Lift Station Text |  | X |  | X |  |
| SAMH | Sanitary Sewer Manhole |  | X |  | X |  |
| SAMHTXT | Sanitary Sewer Manhole Text |  | X |  | X |  |
| SAPIPE | Sanitary Sewer Pipe |  | X |  | X |  |
| SAPIPETXT | Sanitary Sewer Pipe Text |  | X |  | X |  |
| SETBACK | Building Setback Line |  | X |  |  |  |
| SHRUB | Outline of Shrub Areas | X | X |  | X |  |
| SHUTOFF | Utility Shutoffs (natual gas, propane, electrical, water, etc.) | X |  |  |  |  |
| SIDEWALK | Outline of Sidewalks | X | X |  | X |  |
| SIGN | Street Sign |  | X |  | X |  |
| SITENUM | Address Numbers | X |  | X |  |  |
| STAIRS | Stairwell Locations | X |  |  | X |  |
| STARTPT | Starting Point |  | X |  | X |  |
| STBMP | Storm Water BMP |  | X |  | X |  |
| STMH | Manholes and Junction Boxes |  | X |  | X |  |
| STMHTXT | Manholes and Junction Box Text |  | X |  | X |  |
| STPIPE | Storm Pipes and Culverts |  | X |  | X |  |
| STPIPTXT | Culvert and Pipe Text |  | X |  | X |  |
| STRLIT | Street Light |  | X |  | X |  |
| STRNAME | Street Name Text | X | X | X | X |  |
| SUBBOUND | Subdivision Boundary Lines |  | X | X | X |  |
| TANK | Water Tank | X |  |  | X |  |
| TURF | Outline of Turf or Grass Areas | X | X |  | X |  |
| UNITPTS | Unit Locations | X | X |  | X |  |
| WALINE | Water Line |  | X |  | X |  |
| WALINETXT | Water Line Text |  | X |  | X |  |
| WATBOD | Water Bodies (ponds, pool, spa) |  | X |  | X |  |
| WAVAL | Water Valve |  | X |  | X |  |
| WAVALTXT | Water Valve Text |  | X |  | X |  |
| ZONELINE | Zoning Boundary Line |  |  | X |  |  |
| ZONETXT | Zoning Designation |  |  | X |  |  |